Abstract - Accurate localization of a vehicle is a fundamental challenge and one of the most important tasks of mobile robots. This paper describes a stereo visual odometry algorithm for estimating frame-to-frame camera motion from successive stereo image pairs. In this work, we implemented stereo visual odometry using images obtained from KITTI Vision Benchmark Suite and presented obtained results.

Introduction
For autonomous navigation, motion tracking, and obstacle detection and avoidance, a robot must maintain knowledge of its position over time. Vision-based odometry is a robust technique utilized for this purpose. It allows a vehicle to localize itself robustly by using only a stream of images captured by using only a stream of images captured by a camera attached to the vehicle. In robotics and computervision, Visual Odometry is the process of determining the position and orientation of a robot by analyzing the associated camera images. The idea was first introduced for planetary rovers operating on Mars – Moravec in the early 1980s. Visual Odometry  is a technique used to localize a robot by using only a stream of images acquired from a single or multiple cameras attached to the robot. The images contain a sufficient amount of meaningful information (color, texture, shape, etc.) to estimate the movement of a camera in a static environment. Stereo visual odometry estimates the camera's egomotion using a pair of calibrated cameras. Stereo camera systems are inherently more stable than monocular ones because the stereo pair provides good triangulation of image features and resolves the scale ambiguity.

        Related Work

In recent years many algorithms for visual odometry have been developed, which can roughly be devised into two categories, namely methods using monoscopic cameras or methods using stereo rigs. These approaches can be further separated into methods which either use feature matching between consecutive images or feature tracking over a sequence of images. If a calibrated multi-ocular camera setup is available, the 3-dimensional scene can be reconstructed via triangulation. Based on the point clouds of the static scene in two consecutive images, the iterated closest point (ICP) algorithm is often used for egomotion estimation as described in [7]. Monocular cameras mainly require tracking image features (e.g. corners) over a certain number of images. Using these feature tracks, also the scene structure can be computed using structure from motion [8]. In most cases, the multiocular algorithms yield better performances than monocular approaches [4]. Additionaly, if multi-camera approaches are used, the scale ambiguity present in the monocular case is eliminated [1]. Further approaches combine visual odometry with other sensors to increase the accuracy of the results and reduce drift, a problem inherent to all incremental positioning methods.

Overview
 2.1 Dataset used
○ KITTI Vision Benchmark Suite : The KITTI Odometry dataset was used in our project. The dataset contains 21 sequences of stereo video sequences in greyscale.
○ Calibration Files: Camera and projection matrices are provided to the user with every video sequence in the form of a calibration file. Time stamps of every frame is also provided.
○ Poses files: The folder 'poses.txt' contains the ground truth poses (trajectory) for the first 11 sequences.

○ The camera orientation is as follows and shown in Fig. 1 below:
- The X-axis is parallel to the ground and towards the right of the driver.
- The Y-axis is perpendicular to the ground and facing downwards.
- The Z-axis is is parallel to the ground and facing forward

Fig. 1: KITTI dataset recording platform: VW Passat station wagon is equipped with four video cameras (two color and two grayscale cameras), a rotating 3D laser scanner and a combined GPS/IMU inertial navigation system. (Image taken from the KITTI dataset paper)

2.2. Our Approach
The basic algorithm is as follows: for a given pair of frames, (1) detect features in the left image of the first frame (corner detection), (2) track the features to the second frame, (3) calculate disparity and depthmap for the image, especially for the feature points using the right image (4) project the points to 3D using the depths (5) find the largest set of self of consistent matches (inliers), and (4) find the frame-to-frame motion that minimizes the re-projection error for features in the inlier set.
The inlier detection step (3) is the key distinguishing feature of the algorithm. The feature matching stage inevitably produces some incorrect correspondences, which, if left intact, will unfavorably bias the frame-to-frame motion estimate. A common solution to this problem is to use a robust estimator that can tolerate some number of false matches (e.g., RANSAC [4]).

        Fig. 2: Pipeline of Stereo Visual Odometry

3. Detailed Methodology
3.1 Problem Formulation

Input Our input consists of a stream of gray scale images obtained from a stereocamera. In KITTI dataset the input images are already corrected for lens distortion and stereo rectified. Let the pair of images captured at time t and t+1 be (Il,t, Ir,t) and (Il,t+1, Ir,t+1 ) respectively. The intrinsic and extrinsic parameters of the cameras are obtained via any of the available stereo camera calibration algorithms or the dataset.

Output For every stereo image pair we receive after every time step we need to find the rotation matrix R and translation vector t, which together describes the motion of the vehicle between two consecutive frames.

3.2 Disparity maps

It is quite impossible or hard to get the accurate 3D world coordinates of the keypoints from a monocular camera or a single frame of the scene. Like the human eye, we need a pair of stereo images to accurately find the depth of the keypoints in the world. The dataset provides left and right images of each instance.
In case of a stereo camera the coordinate system of the camera is assumed to be situated midway between the two cameras. We will also be considering the left image as the reference image throughout the project. If we are considering a horizontal stereo camera, each matched keypoint will have the same y coordinate. Only the x coordinate of the pixels with the keypoints in left and right images will be different. The difference between these two x coordinates is known as the disparity.

Fig. 3: Geometry for calculating the depth from disparity

To construct disparity map, we have used the StereoSGBM function from OpenCV which is an implementation of Hirschumuller Algorithm. A disparity map is depicted below:

Fig. 4: Stereo disparity map of first sequence image

Using the disparity map, we get the depth of the scene using the formula:

3.3 STFT algorithm for keypoint detection
The keypoint detection function is implemented using SIFT algorithm provided by OpenCV. The SIFT(Scala-Invariant Feature Transformation) algotrithm is a technique introduced by David Lowe in 1999 and is widely used for extracting features of images in the field of computer vision. The SIFT algorithm consists four major steps: Scale-space extrema detedtion; Keypoint localization; Orientation assignment; and Keypoint descripter.
3.3.1 Scale-space extrema detection
  The fisrt step in SIFT algorithm is convoling image with a Guassian kernel to construct an image pyramid, which ensures that each SIFT feature has corresponding relationship at different scale[[i]]. The method is Difference od Guassians(DoG). Given the original image I(x,y), DoG is defined as follows:
[i] ] Abdullah-Al N, Kong Y . Histopathological Breast-Image Classification Using Local and Frequency Domains by Convolutional Neural Network[J]. Information, 2018, 9(1):19-19.

D (x,y,σ)=L(x,y,kσ)−L(x,y,σ)

L(x,y,kσ)=G(x,y,kσ) ＊I(x,y)

where L(x,y,kσ) is obtained by convolution the original image I(x,y) and the Guassian kernel G(x,y,kσ).
3.3.2 Keypoint localization
  Due to the discreteness of scale sapce and pixels, the Duassian difference pyramid is also discrete. Some potential keypoints are therefore unstable. Talyor series expansion is used to determine the position of keypoints. The Taylor expansion is given by:

f(X) = f( {x } rsub {0 } ) + {∂ {f } ^ {T } } over {∂ X } X + {1 } over {2 } {X } ^ {T } {{∂ } ^ {2 } f } over {∂ {X } ^ {2 } } X
where X=(x,y,σ) and f is Difference of Guassians. The derivative is:

{∂ f(X) } over {∂ X } = {∂ {f } ^ {T } } over {∂ X } + {{∂ } ^ {2 } f } over {∂ {X } ^ {2 } } X
Let it be 0 and the position of extreme points can be obtained.
3.3.3 Orientation assigment
  The algorithm adopts gradient histogram method. It calculates the gradient of pixels firstly within a cell. After completing the gradient calculation of the keypoints, it uses the histogram to count the gradient and direction of the pixels in the neighborhood. The gradient histogram divides the direction range from 0 to 360 degrees into 36 bins, each of which represents a range of 10 degrees.
3.3.4 Keypoint descripter
  In this step, the patch is divided into 4×4 blocks, each of which is 16×16 pixels. Each block has an 8-bin histogram to store the gradient orientations. Histogram increases by weighted magnitude for each gradient.
  The keypoint detection function converts the image to gray and then uses it as input of SIFT function. It returns the coordinate of kepoints. One input and output images are shown as follows:

        Figure 1. Original image

Figure 2. Output of SIFT

3.4 Feature bucketing
  Feature bucketing is a method that ensures feature points are well distributed in image and reduces computation complexity of algorithm. It divides the image into several cells, which are called buckets. For each bucket, it selects 10 points with strongest response and then return the coordinte of keypoint after bucketing. Response indiactes how good the keypoints are. The strongest response corresponds the best keypoint. The followwing is the ouput of feature bucketing method:

Figure 3. Ouput of bucketing

Compared with Figure 2, the number of keypoinys in Figure 3 is reduced.
3.5 Feature tracking
  Feature tracking is a problem to track keypoints in an image sequence, which can be used for motion analysis, object tracking, etc. One of the important method is called Lucas-Kanade method, which is based on Optical Flow.
3.5.1 Optical Flow
  Suppose the pixel (x,y) at T moves to (x+dx,y+dy) after time dt. According to britness consistancy:

I(x,y,t)=I(x+dx,y+dy,t+dt)
where I(x,y,t) is britness of pixel (x,y) at time t. Applying Taylor expansion:
I(x+dx,y+dy,t+dt)
=I(x,y,t)+ {∂ I } over {∂x } Δ x + {∂ I } over {∂ y } Δ y + {∂ I } over {∂ t } Δ t
then we have:
{∂ I } over {∂x } Δ x + {∂ I } over {∂ y } Δ y + {∂ I } over {∂ t } Δ t=0

{∂ I } over {∂x } {Δ x } over {Δ t } + {∂ I } over {∂ y } {Δy } over {Δ t } + {∂ I } over {∂ t } {Δ t } over {Δ t } =0
and the Optical flow equation is:
{I } rsub {x } {V } rsub {x } + {I } rsub {y } {V } rsub {y } + {I } rsub {t } =0
3.5.2 Lucas-Kanade method
The main principle of Lucas-Kanade optical flow estimation is to assume constant brightness to find the velocity vector between two consecutive frames (t and t+1)[[ii]] by the following equation:
[ii] [] O. Haggui, C. Tadonki, F. Sayadi and B. Ouni, "Evaluation of an OPENMP Parallelization of Lucas-Kanade on a NUMA-Manycore," 2018 30th International Symposium on Computer Architecture and High Performance Computing (SBAC-PAD), Lyon, France, 2018, pp. 436-441, doi: 10.1109/CAHPC.2018.8645936.
left [matrix {{I } rsub {x } ( {p } rsub {1 } ) # {I } rsub {y } ( {p } rsub {1 } ) ## ⋮ # ⋮ ## {I } rsub {y } ( {p } rsub {n } ) # {I } rsub {y } ( {p } rsub {n } ) } right ] [ matrix {{V } rsub {x } ## {V } rsub {y } } ]=[ matrix {{− I } rsub {t } ( {p } rsub {1 } ) ## ⋮ ## {−I } rsub {t } ( {p } rsub {n } ) } ]

Python library OpenCV provide a function calcOpticalFlowPyrLK(), which implements Lucas-Kanade method. The function uses the coordinate of keypoints at time t that returned by SIFT function in the last step to calculate the position of the same keypoints at time t+1. It returns the value of status for each input point. If the corresponding keypoint is found, the value of status will be 1.
After that, the feature tracking function will return the coordianate of corresponding points with status equal to 1. The data obtained will be used to generate 3D point cloud.

3.6 projecting feature points to camera coordinate system
Using the depthmap that was calculated from the disparity map, the depth of the feature points in the left image is extracted. Using the projection matrix and the depth, the points are projected from the screen of left camera to the 3-dimensional coordinate system of the left camera.
Fig. 1 shows the orientation of the camera coordinate system in red. The z- coordinates comes out of the image plane and is pointing forwards. The y-axis is pointing downwards and the x-axis is pointing to the right.

  1. Inlier detection
For the estimation of the RT matrix, only the points should be considered where no errors in tracking or triangulation occur and that are not moving relative to other points. The distance of the 3D points relative to each other point should not change when moving the camera. This fact is used for a inlier detection with the clique algorithm. This algorithm was also used in the paper. First, the distance of the n 3D points in frame 1 to each other is calculated and stored in a nxn dimensional array, same for the points in frame 2. This two arrays are subtracted. A critical difference (e.g. 0.2m) is chosen. The whose distance to the most other points does not change (difference less than critical difference) is added to the clique first. After that, step by step new points are added to the clique. Potential inliers are all points with a distance difference of less than d_crit with all points in the clique. In each step, the potential inlier that is consistent with most other potential inliers is added to the clique.

  1. Estimating the transformation matrix
The transformation of the camera position between two frames is given by 6 parameters: 3 rotational and 3 translational. The rotation part is described by a rotation matrix that is a product of 3 rotation matrices around x, y and z axis. The translation is added. The complete transformation is given by a 4x4 dimensional Matrix:

The 6 parameters of the matrix are estimated using least squares. The 3-dimensional points in camera position 1 are transformed to the cooredinate system of camera position 2 using the RT Matrix and projected to the screen in position 2 using the projection matrix. The error function is the sum of the squared distances of the points projected to screen in position 2 to the tracked points in the image. This error function is used for least squares. Using the optimized parameters, the RT matrix of the step is calculated. The inverse RT matrix is multiplied from the right side to the matrix of all the steps before to get the total position. The most interesting thing about the matrix is the last column which shows the tracked position of the camera.
  1. RANSAC
Instead of the inlier detection, RANSAC can be used. Here, in each iteration 6 random pairs of points (6 3D points in frame 1, 6 2D points in frame 2) are selected. The RT-Matrix is calculated using these 6 points. Using this matrix, the reprojection error of all other points is calculated and the number of point pairs that give an error smaller than a critical value is counted. In the end, the RT-Matrix from the iteration with the most matching point pairs is used.

Stereo Visual Odometry Results
The algorithm is applied to the KITTI odometry dataset (sequence 00) and the camera trajectory computed from the images is plotted together with the true trajectory. Especially for the first 500 frames, the camera trajectory computed by visual odometry is near to the true trajectory. Later, the errors in rotation add up and the trajectory is rotated (in the end about 45 degrees after 4000 frames) compared to the true one. This problem ocours becaurse the camera movement is calculated from frame to frame and a rotation error in a single frame can influence all the trajectory afterwards very strong.
A video with the results for 4000 including tracked feature points, depthmap and camera trajectory has been produced.

Figure 1: camera trajectory from visual odometry (red) and true trajectory (green) for 1000 frames using clique inlier detection

Also, experiments with RANSAC instead of inlier detection have been done. This algorithm takes much time, even with only 200 RANSAC-iterations. The resulting trajectory after 300 images is a little bit better than for inlier detection.

Figure 2: camera trajectory from visual odometry and true trajectory for 300 frames using RANSAC

1. Experiments,
2. Findings,
3. Conclusion

[1] M. Agrawal and K. Konolige, “Real-time localization in outdoor environments using stereo vision and inexpensive gps,” in Proceedings of the 18th International Conference on Pattern Recognition, 2006, pp. 1063 – 10 068.
[4] H. Badino, “A robust approach for ego-motion estimation using a mobile stereo platform,” in First International Workshop on Complex Motion, 2004, pp. 198 – 208.

[7] A. Milella and R. Siegwart, “Stereo-based ego-motion estimation using pixel-tracking and iterative closest point,” in Proceedings of the Fourth IEEE International Conference on Computer Vision Systems, 2006.
[8] D. Nister, O. Naroditsky, and J. Bergen, “Visual odometry,” in ´ IEEE Computer Society Conference Computer Vision and Pattern Recognition, vol. 1, 2004, pp. 652 – 659.